2.5-Dimethylphenol

1、CERTIFICATION OF ANALYSIS:

Properties: Almost white to creamy-pink columnar crystal or flake solid, easily soluble in alcohol and ether. It can be sublimated and volatilized with water vapor.

Enterprise standard No.Q/HHO/P02-1999

| ITEM | TEST |
| --- | --- |
| Description | Almost white to creamy-pink columnar crystal or flake solid |
| Moisture | 0.1% |
| Melting point | 74.0℃-77.0℃ |
| Purity | 99.0% |
| Isomersand homologue | 1.0% |

Uses: used for making gemfibrozil and intermediates of dye.

Packing: Packed in a plastic woven sack lined with two layers polyethylene inflation film sacks, net weight 25.0kgs.

Remark: the product can be packed with other method according to customer's requirement.

2、MSDS

**** SECTION 1 - CHEMICAL PRODUCT AND COMPANY IDENTIFICATION ****

MSDS Name: 2,5-Dimethylphenol, 99+%

Catalog Numbers:

AC116540000, AC116540050, AC116541000, AC116545000

Synonyms:

2,5-Xylenol; 1,4-Dimethyl-2-Hydroxybenzene;

1-Hydroxy-2,5-Dimethylbenzene; 2,5-Xylenol; P-Xylenol.

Company Identification (Europe):  Acros Organics BVBA

Janssen Pharmaceuticalaan 3a

2440 Geel, Belgium

Company Identification (USA):     Acros Organics

One Reagent Lane

Fairlawn, NJ  07410

For information in North America, call:   800-ACROS-01

For information in Europe, call:          0032(0) 14575211

For emergencies in the US, call CHEMTREC: 800-424-9300

For emergencies in Europe, call:     0032(0) 14575299

**** SECTION 2 - COMPOSITION, INFORMATION ON INGREDIENTS ****

+----------------+--------------------------------------+----------+-----------+

|      CAS#      |              Chemical Name           |    %     |  EINECS#  |

|----------------|--------------------------------------|----------|-----------|

|       95-87-4  |2,5-Dimethylphenol                    |   99+%   | 202-461-5 |

+----------------+--------------------------------------+----------+-----------+

Hazard Symbols: XN

Risk Phrases: 21/22

**** SECTION 3 - HAZARDS IDENTIFICATION ****

EMERGENCY OVERVIEW

Harmful in contact with skin and if swallowed.

Potential Health Effects

Eye:

Causes eye irritation.  May cause conjunctivitis and corneal

inflammation.

Skin:

Causes skin irritation.

Ingestion:

Harmful if swallowed. May cause irritation of the digestive tract.

May cause kidney damage. Human fatalities have been reported from

acute poisoning.

Inhalation:

May cause respiratory tract irritation.

Chronic:

Chronic ingestion may cause effects similar to those of acute

ingestion.

**** SECTION 4 - FIRST AID MEASURES ****

Eyes:

Immediately flush eyes with plenty of water for at least 15 minutes,

occasionally lifting the upper and lower eyelids. Get medical aid

immediately.

Skin:

Get medical aid. Immediately flush skin with plenty of soap and

water for at least 15 minutes while removing contaminated clothing

and shoes. Wash clothing before reuse.

Ingestion:

Do NOT induce vomiting. If victim is conscious and alert, give 2-4

cupfuls of milk or water. Never give anything by mouth to an

unconscious person. Get medical aid immediately.

Inhalation:

Remove from exposure to fresh air immediately. If not breathing,

give artificial respiration. If breathing is difficult, give oxygen.

Get medical aid. Do NOT use mouth-to-mouth resuscitation.

Notes to Physician:

**** SECTION 5 - FIRE FIGHTING MEASURES ****

General Information:

As in any fire, wear a self-contained breathing apparatus in

pressure-demand, MSHA/NIOSH (approved or equivalent), and full

protective gear. During a fire, irritating and highly toxic gases

may be generated by thermal decomposition or combustion. Dust can be

an explosion hazard when exposed to heat or flame.

Extinguishing Media:

Use water spray, dry chemical, carbon dioxide, or chemical foam.

**** SECTION 6 - ACCIDENTAL RELEASE MEASURES ****

General Information: Use proper personal protective equipment as indicated

in Section 8.

Spills/Leaks:

Clean up spills immediately, observing precautions in the Protective

Equipment section. Sweep up, then place into a suitable container for

disposal. Avoid generating dusty conditions. Provide ventilation.

**** SECTION 7 - HANDLING and STORAGE ****

Handling:

Wash thoroughly after handling. Use only in a well-ventilated area.

Minimize dust generation and accumulation. Do not get in eyes, on

skin, or on clothing. Keep container tightly closed. Avoid contact

with heat, sparks and flame. Do not ingest or inhale.

Storage:

Keep away from heat, sparks, and flame. Keep away from sources of

ignition. Store in a tightly closed container. Store in a cool, dry,

well-ventilated area away from incompatible substances.

**** SECTION 8 - EXPOSURE CONTROLS, PERSONAL PROTECTION ****

Engineering Controls:

Facilities storing or utilizing this material should be equipped

with an eyewash facility and a safety shower. Use adequate

ventilation to keep airborne concentrations low.

Personal Protective Equipment

Eyes:

Wear appropriate protective eyeglasses or chemical

safety goggles as described by OSHA's eye and face

protection regulations in 29 CFR 1910.133 or European

Standard EN166.

Skin:

Wear appropriate protective gloves to prevent skin

exposure.

Clothing:

Wear appropriate protective clothing to prevent skin

exposure.

Respirators:

Follow the OSHA respirator regulations found in 29CFR

1910.134 or European Standard EN 149. Always use a

NIOSH or European Standard EN 149 approved respirator

when necessary.

**** SECTION 9 - PHYSICAL AND CHEMICAL PROPERTIES ****

Physical State:             Solid

Appearance:                 not available

Odor:                           Characteristic phenolic odor

pH:                              Not available.

Vapor Pressure:           10 mm Hg @91.3C

Vapor Density:            Not available.

Evaporation Rate:        Not available.

Viscosity:                    cP75C

Boiling Point:              212 deg C

Freezing/Melting Point:       74.5 deg C

Autoignition Temperature:   555 deg C ( 1,031.00 deg F)

Flash Point:                          73 deg C ( 163.40 deg F)

Explosion Limits, lower:     1.40 vol %

Explosion Limits, upper:     Not available.

Decomposition Temperature:

Solubility:                           4.6g/L

Specific Gravity/Density:   0 .9710

Molecular Formula:           C8H10O

Molecular Weight:             122.17

**** SECTION 10 - STABILITY AND REACTIVITY ****

Chemical Stability:

Stable under normal temperatures and pressures.

Conditions to Avoid:

Incompatible materials, dust generation, excess heat.

Incompatibilities with Other Materials:

Bases - acid chlorides - acid anhydrides - oxidizing agents -

corrodes steel - brass - copper - copper alloys.

Hazardous Decomposition Products:

Carbon monoxide, carbon dioxide.

Hazardous Polymerization: Will not occur.

**** SECTION 11 - TOXICOLOGICAL INFORMATION ****

RTECS#:

CAS# 95-87-4: ZE5775000

LD50/LC50:

CAS# 95-87-4: Oral, mouse: LD50 = 383 mg/kg; Oral, rabbit: LD50 =

938 mg/kg; Oral, rat: LD50 = 444 mg/kg.

Carcinogenicity:

2,5-Dimethylphenol -

Not listed by ACGIH, IARC, NIOSH, NTP, or OSHA.

Epidemiology:

Experimental tumorigenic effects have been reported.

Teratogenicity:

No information found.

Reproductive Effects:

No information found.

Neurotoxicity:

No information found.

Mutagenicity:

No information found.

Other Studies:

See actual entry in RTECS for complete information.

**** SECTION 12 - ECOLOGICAL INFORMATION ****

Ecotoxicity:

cfr. Genium

**** SECTION 13 - DISPOSAL CONSIDERATIONS ****

Dispose of in a manner consistent with federal, state, and local regulations.

**** SECTION 14 - TRANSPORT INFORMATION ****

US DOT

Shipping Name: XYLENOLS

Hazard Class: 6.1

UN Number: 2261

Packing Group: II

Canadian TDG

Shipping Name: XYLENOLS

Hazard Class: 6.1(9.2)

UN Number: UN2261

**** SECTION 15 - REGULATORY INFORMATION ****

US FEDERAL

TSCA

CAS# 95-87-4 is listed on the TSCA inventory.

This material does not contain any Class 2 Ozone depletors.

Clean Water Act:

None of the chemicals in this product are listed as Hazardous

Substances under the CWA.

None of the chemicals in this product are listed as Priority

Pollutants under the CWA.

None of the chemicals in this product are listed as Toxic Pollutants

under the CWA.

OSHA:

None of the chemicals in this product are considered highly hazardous

by OSHA.

STATE

2,5-Dimethylphenol is not present on state lists from CA, PA, MN, MA,

FL, or NJ.

California No Significant Risk Level:

None of the chemicals in this product are listed.

European/International Regulations

European Labeling in Accordance with EC Directives

Hazard Symbols: XN

Risk Phrases:

R 21/22  Harmful in contact with skin and if

swallowed.

Safety Phrases:

S 2  Keep out of reach of children.

S 28A  After contact with skin, wash immediately with

plenty of water.

S 45  In case of accident or if you feel unwell, seek

medical advice immediately (show the label where

possible).

WGK (Water Danger/Protection)

CAS# 95-87-4: 2

United Kingdom Occupational Exposure Limits

Canada

CAS# 95-87-4 is listed on Canada's DSL List.

CAS# 95-87-4 is not listed on Canada's Ingredient Disclosure List.

Exposure Limits

**** SECTION 16 - ADDITIONAL INFORMATION ****

MSDS Creation Date:  9/17/1997  Revision #2 Date:  8/02/2000

The information above is believed to be accurate and represents the best

information currently available to us. However, we make no warranty of

merchantability or any other warranty, express or implied, with respect to

such information, and we assume no liability resulting from its use. Users

should make their own investigations to determine the suitability of the

information for their particular purposes. In no way shall the company be

liable for any claims, losses, or damages of any third party or for lost

profits or any special, indirect, incidental, consequential or exemplary

damages, howsoever arising, even if the company has been advised of

the possibility of such damages.

--------------------------------------------------------------------------------