ORTHO-XYLENE

NAME:ortho-xylene

CAS:95-47-6

ICSC:

CHARACTERISTICS TYPICAL VALUE SPECIFICATION TEST METHOD Color (Pt-Co Scale) 5 Max. 20 ASTM D 1209 Specific Gravity, 15.56-15.56°C 0.882~0.885 0.882~0.885 ASTM D 4052 Component Analysis - Purity, wt. % - Non-Aromatics - P-Xylene - Meta-Xylene - BZ+C9+ARO 98.5 03 0.3 1.0 1.0 Min. 98.0 Max. 0.7 Max. 0.5 Max. 1.5 Max. 1.5 UOP 744 Acid Wash Color Nil Max. 2.0 ASTM D 848 Sulfur Compounds None Detected None Detected ASTM D 853 Acidity None Detected None Detected ASTM D 847 Total Distillation Range at 760 mmHge Pressure 1.0°C Not more than2°C including the temperature of 144.4°C ASTM D 850 Application Manufacture of Phthalic Anhydride Vitamin and Pharmaceutical synthesis Dyes, insecticides, motor fuels